## Slide 1
EEG Pain Biomarker Pipeline — Overview
Slide 1 — Title

## Slide 2
Slide 2
Slide 2 — Goals
Identify robust EEG biomarkers that discriminate pain vs no‑pain
Produce leakage-safe held‑out validation (LOSO)
Provide a deployable, interpretable model and an audit trail for reproducibility
Notes: Slide 2
Slide 2 — Goals
Identify robust EEG biomarkers that discriminate pain vs no‑pain
Produce leakage-safe held‑out validation (LOSO)
Provide a deployable, interpretable model and an audit trail for reproducibility

## Slide 3
Slide 3
Slide 3 — Dataset & Key facts
OpenNeuro ds005284 (Zhao et al.), Biosemi 64-channel, 1024 Hz (resampled to 256 Hz)
26 subjects, 781 epochs (367 pain / 414 no‑pain)
ROI: C3, CZ, C4 focused on somatosensory responses
Notes: Slide 3
Slide 3 — Dataset & Key facts
OpenNeuro ds005284 (Zhao et al.), Biosemi 64-channel, 1024 Hz (resampled to 256 Hz)
26 subjects, 781 epochs (367 pain / 414 no‑pain)
ROI: C3, CZ, C4 focused on somatosensory responses

## Slide 4
Slide 4
Slide 4 — Preprocessing pipeline (exact steps)
1. Channel mapping: map raw device labels → 10–20 (channels.tsv)
2. Resample: 1024 → 256 Hz
3. Notch: 50 Hz & 100 Hz (adjust to 60 Hz mains if needed)
4. Bandpass: 0.5 – 80 Hz
5. Reference: average reference
6. Epoching:
Pain: 0 → +2 s relative to stimulus onset
No‑pain baseline: −5 → −3 s
7. Artifact rejection: amplitude threshold (|µV| > 200)
8. Save per-epoch QC and per-subject summaries (audit CSVs)
Notes: Slide 4
Slide 4 — Preprocessing pipeline (exact steps)
1. Channel mapping: map raw device labels → 10–20 (channels.tsv)
2. Resample: 1024 → 256 Hz
3. Notch: 50 Hz & 100 Hz (adjust to 60 Hz mains if needed)
4. Bandpass: 0.5 – 80 Hz
5. Reference: average reference
6. Epoching:
Pain: 0 → +2 s relative to stimulus onset
No‑pain baseline: −5 → −3 s
7. Artifact rejection: amplitude threshold (|µV| > 200)
8. Save per-epoch QC and per-subject summaries (audit CSVs)

## Slide 5
Slide 5
Slide 5 — Feature families (extract all for new datasets)
Spectral: abs/rel band power (δ,θ,α,β,low‑γ), band ratios, spectral centroid, median freq, 1/f slope
Nonlinear: Higuchi FD, Petrosian FD, DFA, sample & permutation entropy, Lempel‑Ziv, Hjorth
Time-domain: RMS, STD, peak‑to‑peak, line length, zero-crossing rate, skew, kurtosis
Wavelet: db4 multiscale energy ratios, wavelet entropy
MFCC: first 5 MFCC means per channel
AR dynamics: Burg AR coefficients + innovation variance
Connectivity: coherence & PLV for C3-CZ, C3-C4, CZ-C4 across bands
Notes: Slide 5
Slide 5 — Feature families (extract all for new datasets)
Spectral: abs/rel band power (δ,θ,α,β,low‑γ), band ratios, spectral centroid, median freq, 1/f slope
Nonlinear: Higuchi FD, Petrosian FD, DFA, sample & permutation entropy, Lempel‑Ziv, Hjorth
Time-domain: RMS, STD, peak‑to‑peak, line length, zero-crossing rate, skew, kurtosis
Wavelet: db4 multiscale energy ratios, wavelet entropy
MFCC: first 5 MFCC means per channel
AR dynamics: Burg AR coefficients + innovation variance
Connectivity: coherence & PLV for C3-CZ, C3-C4, CZ-C4 across bands

## Slide 6
Slide 6
Slide 6 — Feature naming & storage
Use descriptive names: e.g., CZ_higuchi, C3_alpha_power, CZ_C4_lowgamma_plv
Save:
features CSV (rows = epochs, cols = features)
features NPZ (X, y, subjects, feature_names)
per-epoch QC CSV and subject_summary.csv
Notes: Slide 6
Slide 6 — Feature naming & storage
Use descriptive names: e.g., CZ_higuchi, C3_alpha_power, CZ_C4_lowgamma_plv
Save:
features CSV (rows = epochs, cols = features)
features NPZ (X, y, subjects, feature_names)
per-epoch QC CSV and subject_summary.csv

## Slide 7
Slide 7
Slide 7 — Validation (leakage-safe procedure)
1. Use Leave‑One‑Subject‑Out (LOSO) or appropriate grouped CV
2. For each training fold:
Replace non-finite, apply variance threshold (train-only)
Fit StandardScaler (train-only) → transform test
Compute ANOVA-F ranking on train → select top‑K (e.g., K=60)
Fit classifier (e.g., LDA with shrinkage)
3. Predict on held‑out subject; collect per-fold AUCs, sensitivities, specificities
4. Report mean AUC ± SD and per-subject metrics; use paired tests for ablations (Wilcoxon)
Notes: Slide 7
Slide 7 — Validation (leakage-safe procedure)
1. Use Leave‑One‑Subject‑Out (LOSO) or appropriate grouped CV
2. For each training fold:
Replace non-finite, apply variance threshold (train-only)
Fit StandardScaler (train-only) → transform test
Compute ANOVA-F ranking on train → select top‑K (e.g., K=60)
Fit classifier (e.g., LDA with shrinkage)
3. Predict on held‑out subject; collect per-fold AUCs, sensitivities, specificities
4. Report mean AUC ± SD and per-subject metrics; use paired tests for ablations (Wilcoxon)

## Slide 8
Slide 8
Slide 8 — Recommended classifiers & deployment
Research / exploration: RF / Gradient Boosting for ablation; check overfitting
Deployment / interpretability: LDA (shrinkage) on parsimonious set (e.g., top nonlinear CZ features)
Implement per-subject QC gating before decision-making
Notes: Slide 8
Slide 8 — Recommended classifiers & deployment
Research / exploration: RF / Gradient Boosting for ablation; check overfitting
Deployment / interpretability: LDA (shrinkage) on parsimonious set (e.g., top nonlinear CZ features)
Implement per-subject QC gating before decision-making

## Slide 9
Slide 9
Slide 9 — Ablation strategy
Baseline (135 features) vs Baseline + family (wavelet / MFCC / AR / connectivity)
Use the same LOSO splits and compute paired Wilcoxon tests across folds
Record fold-level outputs and config JSON for auditability
Notes: Slide 9
Slide 9 — Ablation strategy
Baseline (135 features) vs Baseline + family (wavelet / MFCC / AR / connectivity)
Use the same LOSO splits and compute paired Wilcoxon tests across folds
Record fold-level outputs and config JSON for auditability

## Slide 10
Slide 10
Slide 10 — Typical outputs & audit files
all_subjects_features.csv, features_xy.npz, classification_results.csv
per_subject_accuracy.csv, subject_summary.csv
biomarker_exploration_screening.csv, biomarker_loso_ablation_results.csv
Figures: ROC curves, feature heatmaps, per-subject violin plots
Notes: Slide 10
Slide 10 — Typical outputs & audit files
all_subjects_features.csv, features_xy.npz, classification_results.csv
per_subject_accuracy.csv, subject_summary.csv
biomarker_exploration_screening.csv, biomarker_loso_ablation_results.csv
Figures: ROC curves, feature heatmaps, per-subject violin plots

## Slide 11
Slide 11
Slide 11 — Action items for a new dataset
Prepare channels.tsv; verify event structure and stimulus timing
Run preprocessing; save QC; extract baseline 135 features
Run LOSO with training-only scaling & selection; run family ablations
If stable biomarkers appear, retrain compact model for deployment; validate on external dataset if available
Notes: Slide 11
Slide 11 — Action items for a new dataset
Prepare channels.tsv; verify event structure and stimulus timing
Run preprocessing; save QC; extract baseline 135 features
Run LOSO with training-only scaling & selection; run family ablations
If stable biomarkers appear, retrain compact model for deployment; validate on external dataset if available

## Slide 12
Slide 12
Slide 12 — Contact / Next steps
Commit run outputs and config JSON for every experiment
Add subject-level QC thresholds and automated gating
Move toward real-time inference test with LDA on streaming ROI signals
Notes: Slide 12
Slide 12 — Contact / Next steps
Commit run outputs and config JSON for every experiment
Add subject-level QC thresholds and automated gating
Move toward real-time inference test with LDA on streaming ROI signals

## Slide 13
Slide 13
Notes: Slide 13